## Slide 1
Lumio
An Intelligent Educational Classroom Robot Platform
Sameed Ahmed • 2VX22CB043
B.Tech – Computer Science and Business Systems
Visvesvaraya Technological University, Belagavi
SonyTech IT Company
R.A.D.G.T.F Foundation
2025–2026

## Slide 2
THE PROBLEM
Why do existing educational robots fall short?
Closed & Proprietary
Locked hardware and software prevent schools from extending or understanding what runs on them.
No Real AI
Existing kits lack modern AI: no on-device LLM, no vision, no natural language — just scripted commands.
Cloud Dependent
Most AI features require internet connectivity — unreliable in real classrooms and unacceptable for data privacy.
Lumio addresses all three — open hardware, embedded AI, fully offline.

## Slide 3
LUMIO AT A GLANCE
Three integrated layers — hardware, firmware, software
APPLICATION LAYER
Raspberry Pi 5 — Debian Linux
Multi-threaded Python: voice interaction, LLM inference (Ollama phi3:mini), Piper TTS, wireless control, AI vision (in progress)
CO-PROCESSOR LAYER
RP2040 — MicroPython Firmware
GPIO expansion, ADC telemetry, display management. JSON command protocol over UART with RPi 5.
HARDWARE LAYER
Lumio V2 PCB — KiCad 9.0
4-layer custom PCB: LM2577 boost, L298N motor driver, MCP3008 ADC, 8× sensor headers, QWIIC I2C, HC-SR04 ports.

## Slide 4
HARDWARE ARCHITECTURE
Lumio V2 PCB — 4-layer, 115mm × 73mm, JLCPCB PCBA
Power Management
LM2577 boost: 5V → 12V
DFRobot UPS powers RPi 5
3 voltage domains: 3V3, 5V, 12V
Motor Control
L298N H-bridge (dual channel)
SS34B freewheel diodes
PWM from RPi 5 GPIO ribbon
Analog Sensing
MCP3008 8-ch 10-bit SPI ADC
8× 3-pin sensor headers
100nF bypass on each VCC
RP2040 Sub-system
QFN-56 co-processor
W25Q64 8MB SPI flash
12MHz HC-49SMD crystal
Connectivity
4× I2C ports (QWIIC + JST-PH)
2× HC-SR04 ultrasonic
40-pin GPIO ribbon to RPi 5
Display / Vision
DSI display (native RPi FW)
Replaced I2C HAT (V1)
CSI camera for AI vision

## Slide 5
RP2040 CO-PROCESSOR
GPIO expansion + telemetry + field-programmable via USB
Key Components
RP2040 QFN-56 • Dual Cortex-M0+ @ 133MHz
W25Q64 SPI Flash • 8MB program storage (QSPI)
12MHz HC-49SMD crystal • 33pF load caps
USB-C + 5.1kΩ CC resistors • BOOTSEL mode
27Ω D+/D– impedance matching • USB 1.1
SW1 BOOTSEL + SW2 RESET tactile switches
1µF + 100nF decoupling on all power pins
UART JSON Protocol
RPi 5 → RP2040:
{"action": "set", "pin": 5, "value": 1}
{"action": "adc_read", "channel": 3}
RP2040 → RPi 5:
{"status": "ok", "value": 712}
Why MicroPython?
Field-programmable via Thonny + USB mass storage boot — no cross-compilation toolchain needed. Non-specialist staff can update firmware in the classroom without removing the board.

## Slide 6
AI SOFTWARE STACK
100% offline AI — no cloud dependency
USB Mic
PyAudio
16kHz mono
Wake Word
Lightweight
keyword gate
Vosk STT
Offline ASR
ARM-optimised
Ollama LLM
phi3:mini
3.8B params
Piper TTS
Neural TTS
no network
Multi-threaded Python Architecture
VoiceCommandListener
Wake word → Vosk → Ollama → Piper pipeline running on its own daemon thread.
MotorControlThread
Translates high-level directives (forward/turn/stop) into PWM GPIO signals for L298N.
WirelessControl
Bluetooth/WiFi remote control via RPi 5's onboard wireless — replaces Google Sheets polling demo.

## Slide 7
KEY DESIGN DECISIONS
Each choice driven by real classroom constraints
✓ DSI
DSI vs I2C Display
I2C HAT required fragile custom framebuffer kernel drivers. DSI is natively supported by RPi firmware — no driver work, higher resolution, better refresh.
✓ RP2040
RP2040 vs GPIO Expander IC
A plain MCP23017 expander only gives extra pins. RP2040 adds programmable logic, hardware PWM, MicroPython runtime, and independent field-update capability.
✓ SS34B Schottky
SS34B vs 1N4148 Diodes
1N4148 is rated 300mA — undersized for motor flyback. SS34B handles 3A continuous and has faster recovery time appropriate for PWM H-bridge switching.
✓ Fully offline
On-device AI vs Cloud AI
Classroom internet is unreliable. Cloud latency breaks real-time voice interaction. phi3:mini + Vosk + Piper all run on RPi 5 without GPU acceleration.

## Slide 8
BILL OF MATERIALS
Core components — selected for JLCPCB PCBA compatibility
Reference
Part
Description
U1
MCP3008-I/SL
8-ch 10-bit SPI ADC, SOIC-16 narrow
U2
LM2577T-ADJ
Boost regulator 5V→12V, TO-220-5
U3
L298N
Dual H-bridge motor driver, TO-220-15
U4
W25Q64JVXGIQ
8MB SPI flash for RP2040, DFN-8
U5
RP2040
Dual-core Cortex-M0+ co-processor, QFN-56
Y1
12MHz HC-49SMD
Crystal oscillator, 33pF load caps
D1–D9
SS34B
3A Schottky, SMA — freewheel & boost diodes
C33
680µF Polymer
Boost output bulk filter capacitor
J1
2×20 Pin Header
RPi 5 40-pin GPIO extension ribbon
J4, J5
JST-SH 4P (QWIIC)
I2C expansion — SparkFun QWIIC ecosystem
J14
USB-C 14P
RP2040 USB — BOOTSEL firmware flashing

## Slide 9
DEVELOPMENT JOURNEY
Four iterations from concept to fabrication-ready design
01
Schematic Capture
KiCad Eeschema, component selection (LM2577, MCP3008, SS34B), RP2040 co-processor added for GPIO expansion
02
PCB Layout & DRC
4-layer routing, power trace widths, crystal trace matching, USB D+/D– diff pair, JLCPCB DRC compliance
03
Software Stack
Vosk + Ollama + Piper pipeline on RPi 5 hardware, RP2040 firmware on Pico, motor control validated vs L298N
04
Display & Integration
I2C HAT → DSI migration, RP2040 UART integration, wireless control, AI vision in active development
Current Status
PCB fully routed and validated in KiCad. Software stack running on RPi 5 hardware. Pending: physical JLCPCB fabrication and AI vision integration.

## Slide 10
RESULTS & ACHIEVEMENTS
All primary objectives met — from schematic to running software
4-Layer
Custom PCB
KiCad 9.0, JLCPCB-ready
8MB
SPI Flash
W25Q64 on RP2040
8-CH
Analog ADC
MCP3008 SPI, 10-bit
3.8B
LLM Params
phi3:mini, on-device
Custom 4-layer PCB fully routed in KiCad with JLCPCB DRC compliance
RP2040 co-processor subsystem with UART JSON protocol to RPi 5
Offline AI voice pipeline: Vosk STT → Ollama phi3:mini → Piper TTS
Motor control, 8-channel ADC, QWIIC I2C, and ultrasonic sensing integrated
DFRobot UPS Module enables battery-backed classroom operation
Open hardware and software throughout — KiCad, Debian, MicroPython

## Slide 11
FUTURE DIRECTIONS & LIMITATIONS
What's next and what we know can be improved
Future Directions
AI Vision: Pi Camera + on-device object & plant species classification
Physical JLCPCB fabrication and hardware bring-up testing
INA219 current sense amplifier for higher-accuracy telemetry
Expanded motor voltage flexibility (software-tunable boost output)
Companion app for wireless Bluetooth/WiFi control interface
Known Limitations
Boost output voltage fixed by R1 ratio — not software-adjustable
RP2040 10-bit ADC limits current sensing precision
AI vision subsystem not yet physically integrated
phi3:mini response quality is suitable but not state-of-the-art

## Slide 12
CONCLUSION
Lumio
Open hardware. Embedded AI. Classroom-ready.
Sameed Ahmed • 2VX22CB043 • SonyTech IT Company / VTU Belagavi
KiCad 9.0
Raspberry Pi 5
RP2040
Ollama phi3:mini
JLCPCB PCBA