## Slide 1
INTERNSHIP REPORT
An 8-month internship report with SonyTech IT Company
Internship Field Report
Sameed Ahmed · 2VX22CB043
SonyTech IT Company · Aug 2025 – Apr 2026
VTU, Belagavi · CSE & Business Systems
🤖

## Slide 2
OVERVIEW
Internship At a Glance
35
Weeks
Aug 2025 – Apr 2026
5
PCB Revisions
V1 → Definitive V2
40+
Test Cases
All passing at close-out
4
Control Pathways
Sheets · IR · BT · WiFi
Project Timeline
Onboarding
& EduTrack
Prototype
& Firmware
PCB V1–V5
Design Arc
Lumio V2
Clean-Sheet
Handover
& Remote
Aug '25 Apr '26

## Slide 3
ORGANIZATION
SonyTech IT Company
SonyTech IT Company
Technology solutions firm specialising in software engineering, embedded systems, and educational technology.
Industry Mentor: Mr. Pranay M Mahendrakar
Location: Bengaluru, Karnataka
R.A.D.G.T.F Foundation
Educational non-profit commissioning the Lumio platform. Focused on innovative tools for classroom learning.
Defined requirements, reviewed prototypes, and guided technical priorities with emphasis on student engagement, safety, and classroom ease-of-deployment.
Academic Context Visvesvaraya Technological University, Belagavi · B.Tech CSE & Business Systems · 2025–2026 · Faculty Mentor: Mr. Rohit B Kaliwal

## Slide 4
THE PROJECT
What is Lumio?
An intelligent, open-hardware educational classroom robot — built from first principles.
🔌
Hardware
Custom 4-layer PCB (Lumio V2) with RP2040 co-processor, L298N motor driver, MCP3008 ADC, LM2577 boost converter, and full sensor array.
⚙️
Firmware
HAL-abstracted multi-threaded Python stack — four concurrent control pathways, queue-arbitrated motor executor, display pipeline.
🧠
On-Device AI
Vosk STT wake-word detection + Ollama (phi3:mini) LLM inference + Piper TTS — fully offline, no cloud dependency.
📊
Google Sheets
Q&A engine and student progress reporting backend — teachers interact through a familiar spreadsheet interface.

## Slide 5
UART Interface
HARDWARE
System Architecture
Raspberry Pi 5
Primary Compute
Lumio V2 PCB
4-layer, 115×73mm
RP2040
Co-Processor
DFRobot UPS
Battery-Backed
DSI Display
Visual Output
Pi Camera
(AI Vision — WIP)
L298N + SS34B
Motor Driver
MCP3008 SPI ADC
8-Channel Sensors
LM2577 Boost
5V → 12V Rail
40-pin ribbon
DSI Cable
Debug Power interface

## Slide 6
PCB DESIGN
PCB Journey: V1 → Definitive V2
V1
Pi Zero 2W
Chassis
Jumper-cable
prototype
→
V2–V5
CM5 Carrier
Exploration
Iterative
hardware arc
→
V2
Final
RPi 5 Platform
Clean-Sheet
DRC-clean
PCBA-ready
Key Design Decisions in Definitive V2
MCP3008 SPI ADC (8-ch) replacing ADS1115 — simpler sensor routing
SS34B Schottky freewheel diodes replacing 1N4148 — correct PWM flyback behaviour
LM2577 boost (5V→12V) with Vout = 1.23 × (1+R1/R2) design-from-equation
RP2040 (QFN-56) with W25Q64 SPI flash, 12MHz crystal, USB-C programming port
DSI display replacing I2C HAT — native RPi firmware framebuffer, no custom driver
Custom KiCad RPi 5 40-pin ribbon header symbol (Conn_02x20_Odd_Even)

## Slide 7
FIRMWARE
Firmware Architecture
Two-layer design: HAL (hardware abstraction) + RobotController (zero GPIO dependency)
LLM Pipeline
Motor Executor
Display Renderer
WiFi Server
Watchdog
Shared Command Queue (threading.Queue + threading.Event arbitration)
Hardware Abstraction Layer (HAL)
MotorHAL · SensorHAL · DisplayHAL
MockHAL (Test Doubles)
Unit tests · Integration tests · Off-hardware CI
4 Control Pathways:
📊 Google Sheets
🔴 Infrared
🔵 Bluetooth
🌐 WiFi Web Panel
v1.1.0 tagged release · All threads with explicit lifecycle management · No command starvation under concurrent load

## Slide 8
RP2040 SUBSYSTEM
RP2040 Co-Processor Subsystem
💾
SPI Flash
W25Q64 on QSPI pins — program storage and runtime data. QSPI traces length-matched during PCB layout.
⏱️
12MHz Crystal
HC-49SMD with correctly calculated 33pF load capacitors (CL=20pF, each cap = 2×CL − stray = 35pF → 33pF std).
🔌
USB-C Port
5.1kΩ CC resistors + 27Ω D+/D− impedance matching. BOOTSEL/RESET tactile switches for programming.
📡
UART Bridge
Communicates with RPi 5 over UART using a lightweight JSON command protocol. Extends GPIO capacity.
QFN-56 thermal pad requires GND via stitching · ERC resolved 18 warnings including floating ADC channels and missing no-connects

## Slide 9
AI INTEGRATION
On-Device AI Voice Pipeline
Fully offline — no cloud dependency. Runs as a dedicated thread alongside all system threads.
🎤
Microphone
Input
Continuous audio
capture
→
👂
Vosk STT
Wake-Word
Offline speech-to-text
detection
→
🧠
Ollama
phi3:mini LLM
Local LLM inference
on RPi 5
→
🔊
Piper TTS
Output
Text-to-speech
response
Zero Cloud Latency
Responses generated locally — classroom deployments with unreliable internet work seamlessly.
Student Q&A
Natural language questions answered semantically, not just keyword matching.
Privacy First
No audio leaves the device — compliant for classroom environments with minors.

## Slide 10
TESTING & QA
Testing & Quality Assurance
40+
integration
test cases
all passing
at close-out
Mock HAL Injection
MockMotorHAL, MockSensorHAL — complete unit tests with zero hardware dependency. Tests run on any machine.
Concurrent Testing
threading.Barrier for synchronised multi-thread test scenarios. Time-frozen assertions via unittest.mock.patch.
Integration Scenarios
Full command pipeline, obstacle abort, emergency stop under all pathways, network outage recovery.
Systematic Design
Equivalence partitioning + boundary value analysis for parser test cases. Severity/effort matrix for debt triage.
HAL abstraction was the single most impactful architectural decision — it made the entire test suite possible.

## Slide 11
CROSS-TEAM WORK
Cross-Team Software Contributions
Weeks 2–3: assisted another SonyTech product team with critical bug fixes in a Flask/SQLite web application (details kept proprietary).
🔒
Concurrency Bug Fix
Traced and resolved a Flask-SocketIO race condition under concurrent client load. Refactored session state to a thread-safe Queue-based architecture, maintaining full backward compatibility.
🗄️
SQL Data Integrity
Fixed a silent data truncation bug in a report export endpoint — no exception raised, identified through careful data comparison. Used SQLite PRAGMA integrity_check during debugging.
📦
Dependency Management
Resolved a transitive Python dependency conflict in requirements. Introduced pip-compile for deterministic builds and transitive dependency pinning.
📋
Structured Logging
Added rotating-file logging across the codebase with structured log levels — replacing ad-hoc print statements and enabling production-grade observability.
Left the codebase in measurably better condition than found — a principle reinforced throughout the internship.

## Slide 12
SKILLS GAINED
Technical Skills Developed
Embedded Hardware
KiCad schematic, PCB layout, DRC, Gerber, JLCPCB PCBA
Boost converter design from voltage equation
Motor flyback & Schottky diode selection
Crystal load capacitor calculation
Staged board bring-up with pass/fail criteria
Firmware & Software
HAL abstraction pattern in Python
Multi-threaded concurrent programming
Custom I2C/SPI sensor drivers from datasheets
Raw-to-SI unit conversion
Semantic versioning & Git conventions
Testing & QA
Dependency-injected mock objects
threading.Barrier for concurrent tests
Equivalence partitioning & BVA
Technical debt severity/effort triage
40+ integration test scenarios
Professional Skills:
Client communication
Scope negotiation
Handover documentation
Remote collaboration
Code review culture

## Slide 13
DELIVERABLES
Deliverables Produced
📦
Lumio Firmware v1.1.0
Tagged & Archived
🔧
PCB V1–V5 (Prototype Arc)
V3 validated production
🖥️
Lumio V2 PCB (Definitive)
DRC-clean, PCBA-ready
✅
Unit & Integration Tests
40+ cases, all passing
📊
Google Sheets Q&A Engine
Delivered
🎞️
GIF Display Pipeline
10 assets, state-synced
🎮
4 Control Pathways
Sheets/IR/BT/WiFi concurrent
📄
Project Handover Document
Architecture + bring-up guide
🐛
EduTrack Bug Fixes
SocketIO, SQL, deps, logging

## Slide 14
CHALLENGES
Challenges & How They Were Overcome
⚠ Framebuffer Driver Conflicts (I2C HAT)
Migrated to DSI display — native RPi firmware support, zero custom driver config required.
⚠ PWM Flyback Destroying 1N4148 Diodes
Replaced with SS34B Schottky (3A, SMA, 0.35V Vf) — correct reverse-recovery behaviour at PWM frequencies.
⚠ HC-49SMD Crystal Misplacement
Discovered load caps connect pin-to-GND only (no GND pins on body) — corrected schematic before layout.
⚠ CM5 Custom-Carrier Complexity
Pivoted to RPi 5 + DFRobot UPS — eliminated custom BMS circuit, accelerated bring-up significantly.
⚠ Concurrent Thread Race Conditions
threading.Event + Queue architecture with explicit lifecycle — tested with threading.Barrier synchronisation.
⚠ Silent SQL Data Truncation
Identified via data comparison + PRAGMA integrity_check; no exception was raised by the original bug.

## Slide 15
Conclusion
35 weeks · End-to-end ownership · Hardware to firmware to handover
Delivered a production-grade educational robot — prototype through five PCB revisions to a definitive, PCBA-ready V2 board
Built a fully testable, HAL-abstracted firmware stack released at v1.1.0 with 40+ passing test cases
Integrated on-device AI (Vosk + Ollama + Piper) for offline natural language Q&A — no cloud dependency
Contributed critical bug fixes to a second proprietary product, leaving the codebase in better condition than found
Developed professional competencies: client communication, scope negotiation, handover documentation, remote collaboration
"This internship confirmed my intent to pursue a career that bridges hardware and software — systems where firmware, PCB design, and product thinking are inseparable disciplines."

## Slide 16
End of Report
Sameed Ahmed
B.Tech CSE & Business Systems · VTU Belagavi
Intern · SonyTech IT Company · Lumio Project
GitHub: github.com/BastaMasta/LumioV2
Queries & Clarifications
🤖